CanFestival3. Version 3.0
The CANOpen stack manual

# Introduction
This document describe the CANOpen layer.CanFestival is an OpenSource (LGPL) CANOpen framework.
This project, initiated by Edouard TISSERANT in 2001, as grown thanks to Francis DUPIN and other contributors.
Today, CanFestival focuses on providing an ANSI-C platform independent CANOpen stack that can be implemented as master or slave nodes on PCs, Real-time IPCs, and Microcontrollers.
CanFestival is a project supported by Lolitech.
# What is CANopen
CANopen is a CAN based high level protocol. It defines some protocols to :
- Configure a CAN network.
- Transmit data to a specific node or in broadcast.
- Administrate the network. For example detecting a not responding node.
The documentation can be found in the Can in automation website :
http://www.can-cia.de/canopen.
The most important document about CANopen is the normative CiA Draft Standard 301, version 4.02. You can now download with no cost the specification in Can in automation website.
To continue reading this document, let us assume that you have read some papers introducing CANopen.
# CanFestival Features
## Tools
The CANopen library is coming with some tools :
- Object Dictionary editor GUI. WxPython Model-View-Controler based GUI, that help a lot in generating object dictionary source code for each node.
- A home made configure script, that let you chose compile time options such as target CPU/HOST and/or CAN,TIMER, LED or NVRAM drivers.
## Standard conformance
### Multi-Platform
- Library source code is C-ANSI.
- Driver and examples coding conventions merely depend on target specific contributor/compiler.
- Unix compatible interfaces and examples should compile and run on any Unix system (tested on GNU/Linux and GNU/FreeBSD).
### CanOpen conformance
- Should be conform to the latest DS301. V.4.02 13 february 2002.
- Master and Slave functionality implemented.
- Sending SYNC implemented.
- 1 SDO server per node.
- Unlimited SDO client.
- SDO transmission mode : normal, expedited download and upload.
- Unlimited PDO receive.
- Unlimited PDO transmit.
- Object Data type implemented : 8, 16, 32 bits values, an fixed length strings.
- Slave state full implemented.
- NMT to change slave's state implemented.
- PDO transmission mode : on request, every reception of 0 to n SYNC, on event.
- NMT Heartbeat implemented : A node can monitor the heartbeats received from others nodes.
- NMT NodeGuard implemented : Not fully implemented.
- TIME (time Stamp) : Not implemented.
- EMCY (emergency objects) : Not implemented.
# How to start
## Host requirements
What you need on your development workstation.
- Linux, FreeBSD, or any Unix with GNU toolchain.
- The GNU C compiler (gcc) or any other ANSI-C compiler for your target platform.
- GNU Make
- Bash
- Python, with wxPyhon modules installed (at least version 2.6.3). You will also need Xpdf, and the official 301_v04000201.pdf file in order to get GUI context sensitive help.
## Linux Targets
Linux target is default configure target. Corresponding configure switch is:
--target=generic
### Normal Linux node
Configure switch:
--timers=unix
To do a CANopen node running on PC-Linux, you need :
- A working linux distribution
- One or more Peak system PC CAN interface and the last Peak Linux driver installed.
### Real-Time Linux node
Configure switch:
--timers=xeno
To do a CANopen node running on PC-Linux, you need :
- A working linux distribution patched with XENOMAI 2.1 or greater.
- One or more Peak system PC CAN interface and the last Peak Real Time Linux driver installed.
### CAN devices
Curently supported CAN devices and corresponding configure switch:
#### Peak systems
Configure switch:
--can=peak
PeakSystems CAN interface is automatically chosen as default CAN interface if libpcan is present in the system.
Please download driver at http://www.peak-system.com/linux and follow instructions in order to install driver on your system.
#### Virtual CAN interfaces (for test/debug)
Configure switch:
--can=virtual
Virtual CAN interface use Unix pipes to emulate a virtual CAN network. Each message issued from a node is repeat to all other nodes. Currently only works with nodes running in the same process, and does not support work with Xenomai.
### Linux Example:
TestMasterSlave :
**************************************************************
* TestMasterSlave *
* *
* A simple example for PC. It does implement 2 CanOpen *
* nodes in the same process. A master and a slave. Both *
* communicate together, exchanging periodically NMT, SYNC, *
* SDO and PDO. *
* *
* If you have chosen virtual CAN driver, just type *
* ./TestMasterSlave *
* *
* Else you need to sepcify bus: *
* *
* -s : slave CAN bus [default 0, peak first PCI] *
* -m : master CAN bus [default 1, peak second PCI] *
* *
**************************************************************
## Motorola HC12
Configure switch:
--target=hcs12
To do a CANopen node running on a microncontroller Motorola MC9S12DP256, you need :
- The compiler GNU gcc for HC12 : m6811-elf.
- A board with this chip. We are using the T-board from Electronikladden. At least about 40 kBytes of program memory.
- A tool to flash the memory. (We are using the hight cost Lauterbach debugger).
### Running a HC12 node
#### Compiling :
./configure --target=hc12
make all
#### Flashing the memory :
Use your prefered loader ! If you are using a debugger Lauterbach, you can load the bash file : trace32_flash_programmer.cmm. It loads directly the elf file.
#### Connecting to a serial RS232 console :
Connect the portS(TxD0) of the HC12 to a console configured at 19200 bauds 8N1, via a Max232 chip to adapt the electricals levels. On Linux, you can use minicom. Connecting to a console is usefull to read the messages, but not required.
#### Connecting to the CAN network :
Connect the port CAN0 (pin PM0, PM1) to the network via a CAN controller. On our board, the CAN controler is a PCA82C250 chip.
#### starting the node :
Press the reset of your HC12 board.
### HCS12 Examples
GeneSync_HCS12 :
An example of HCS12 based CanOpen node sending SYNC messages periodically.
## Compilation
Try to call ./configure –help to see all available compile time options.
After invoking ./configure with your platform specific switches, just type make.
./configure [options]
make
make install
# Developing with CanFestival
## CanFestival Project tree layout
Simplified directory structure.
./src	ANSI-C source files of the CanFestival stack
./drivers	Interface implementation to specific platforms:
./drivers/generic	Generic PC target
./drivers/timers_xeno	Xenomai timers/threads
./drivers/timers_unix	Posix timers/threads
./drivers/can_peak	PeakSystem CAN library interface
./drivers/can_virtual	Fake CAN network
./drivers/hcs12	HCS12 full target interface
./examples	Examples, target specific
./include	Header files, will be installed with binaries
./objdictgen	Object Dictionary editor GUI
./objdictgen/config	Pre-defined OD profiles
./objdictgen/examples	Some examples/test OD
./doc	Project and CanOpen doc
## Developing a new node
Using provided examples as a base for your new node is generally a good idea. You can also use the provided *.od files as a base for your node object dictionary.
### Using Dictionary Editor GUI
#### Usage
cd objdictgen
python objdictedit.py [od files...]
#### About
The Object Dictionary editor GUI is a python application that use the Model-View-Controller design pattern. It depends on WxPython to display view on any supported platform.

#### Main view
Top list let you choose dictionary section, bottom left list is the selected index in that dictionary, and bottom right list are edited sub-indexes.

#### New node
Edit your node name, ID and type. Choose your inherited specific profile.

#### Node info
Edit your node name, ID and type.

#### Profile editor
Chose the used profile to edit.
Pick up optional chosen profile entries.
#### User types
Use User Types to implement value boundaries, and string lentgth
#### Mapped variable
Add your own specific dictionary entries and associated mapped variables.
#### Getting Help
Using F1 key, you can get context sensitive help.
In order to do that, official 301_v04000201.pdf file must be placed into doc/ directory, and xpdf must be present on your system.
F2 key open HTML CanFestival help.
### Generating the object Dictionary
#### With GUI

Then choose C file to create. Header file will be also created with the same prefix.
#### With command line
Usage of objdictgen.py :
python objdictgen.py XMLFilePath CfilePath
# FAQ
## Does the code compiles on Windows ?
Yes, In fact, we use the CANopen layer in a huge project on Windows XP. For the Adlink 7841, we are using the driver provided by Adlink. We have had some problems with it, especially while waiting the messages received on event. Well, we have got round (more or less..) the bugs, and we have done a master node, compiled with Visual Studio C++. We plan to replace the Adlink 7841, while Adlink is not able to distibute a good driver, by a Peaksystem board.
Because some files in the project are in C++, and the CANopen layer in C, I think we have put a compilation option /TC or /TP. See the MSDN documentation about that.
You have to interface the library to the CAN board you are using. To do that, add a new directory in drivers/ and put your code inside, as we have done for HC12 and Linux.
In include, create also a new directory and put the two files applicfg.h, timerhw.h.

## How to fit the library to an other microcontrôler ?
First, be sure that you have at least 40K bytes of program memory, and about 2k of RAM. It is not a such hard work. Be kind not to put specific code for your microcontroler in the code which is target independant. Put a prefix for the object files you create. Example on HC12 :
nmtMaster.c => hc12_nmtMaster.o

## [LINUX] : How to use an other board than Peaksystem board ?
Just install peak driver and then compile and install Canfestival. Peak driver is detected at compile time.
## [HC12] : What board are you using ?
A T-board from elektronikladen with a MC9S12DP256 or MC9S12DG256.

## [HC12] : Does the code compile with an other compiler than GNU gcc ?
It is known to work with Metrowerks CodeWarrior. Here are some tips from Philippe Foureys. :
##### Interrupt functions

###### Code for GCC

// prototype

void __attribute__((interrupt))timer3Hdl(void):

// function
void __attribute__((interrupt))timer3Hdl(void)
{...}

Code for CodeWarrior

// protoype
void interrupt timer3Hdl(void);

// function
pragma CODE_SEG__NEAR_SEG_NON_BANKED
void interrupt timer3Hdl(void)
{...}
pragma CODE_SEG_DEFAULT

###### Interrupt lock, unlock

Code for GCC

void unlock (void)
{
  __asm__ __volatile__("cli");
}

void lock (void)
{
  unsigned short mask;
  __asm__ __volatile__("tpa\n\tsei":"=d"(mask));
}

###### Code for CodeWarrior

void unlock (void)
{
  __asm("cli");
}

void lock (void)
{
  unsigned short mask;
  __asm
 {
  tpa:tsei:"=d"(mask);
 }
}

##### Initialize function

###### Code for GCC

void initCanHCS12 (void)
{
  //Init the HCS12 microcontroler for CanOpen
  initHCS12();
   // Init the HCS12 CAN driver
  const canBusInit bi0 = {
    0, /* no low power */
    0, /* no time stamp */
    1, /* enable MSCAN */
    0, /* clock source : oscillator (In fact, it is not used) */
    0, /* no loop back */
    0, /* no listen only */
    0, /* no low pass filter for wk up */
  CAN_Baudrates[CAN_BAUDRATE_250K],
    {
      0x00, /* Filter on 16 bits. See Motorola Block Guide V02.14 fig 4-3 */
      0x00, 0xFF, /* filter 0 hight accept all msg */
      0x00, 0xFF, /* filter 0 low accept all msg */
      0x00, 0xFF, /* filter 1 hight filter all of msg */
      0x00, 0xFF, /* filter 1 low filter all of msg */
      0x00, 0xFF, /* filter 2 hight filter most of msg */
      0x00, 0xFF, /* filter 2 low filter most of msg */
      0x00, 0xFF, /* filter 3 hight filter most of msg */
      0x00, 0xFF, /* filter 3 low filter most of msg */
    }
  };

###### Code for CodeWarrior

void initCanHCS12 (void)
{
  //Init the HCS12 microcontroler for CanOpen
  initHCS12();
   // Init the HCS12 CAN driver
  const canBusInit bi0 = {
    0, /* no low power */
    0, /* no time stamp */
    1, /* enable MSCAN */
    0, /* clock source : oscillator (In fact, it is not used) */
    0, /* no loop back */
    0, /* no listen only */
    0, /* no low pass filter for wk up */
    {
     1, /* clksrc */
     3, /* brp */
     0, /* sjw */
     0, /* samp */
     1, /* tseg2 */
     12,/* tseg1 */
    },

    {
      0x00, /* Filter on 16 bits. See Motorola Block Guide V02.14 fig 4-3 */
      0x00, 0xFF, /* filter 0 hight accept all msg */
      0x00, 0xFF, /* filter 0 low accept all msg */
      0x00, 0xFF, /* filter 1 hight filter all of msg */
      0x00, 0xFF, /* filter 1 low filter all of msg */
      0x00, 0xFF, /* filter 2 hight filter most of msg */
      0x00, 0xFF, /* filter 2 low filter most of msg */
      0x00, 0xFF, /* filter 3 hight filter most of msg */
      0x00, 0xFF, /* filter 3 low filter most of msg */
    }
  };

## [HC12] : Does the code works in banked memory ?
No. Today it seems that the port of gcc is bogged for using the banked memory. So, unfortunately, we are limited to 48 Kbytes of memory code.

## [HC12] : What GCC version are you using ?
We are using the stable RPM release 2.2 :
- GNU Gcc 3.0.4. Build 20030501
- Newlib 1.10.0 Build 20030421
- GNU Binutils 2.12.1 Build 20030427
Is CanFestival3 conform to DS301 v.4.02 ?
Thanks to Philippe Foureys (IUT of Valence), a slave node have been tested with the National Instrument CanOpen Conformance Test. It passed the test with success.
Some very small unconformity have been found in very unusual situations, for example in the SDO code response to wrong messages.

# Warnings and errors messages management

## Warnings messages

DEBUG _WAR _CONSOLE _ON	DEBUG _CAN	PrintMsg-WarTo-Console		Printing long message on console	Printing short message on console. (number and value only)	Sending number and value in a PDO., only if the node is a slave, in operational state.
DEF	DEF	1			yes
DEF	DEF	0		yes
DEF	UNDEF	1
DEF	UNDEF	0
UNDEF	X	X

## Errors messages

DEBUG _ERR _CONSOLE _ON	DEBUG _CAN	PDO _ERROR	PrintMsg-ErrTo-Console		Printing long message on console	Printing short message on console. (number and value only)	Sending number and value in a PDO., only if the node is a slave, in operational state.
DEF	DEF	X	1			yes	yes
DEF	DEF	X	0		yes		yes
DEF	UNDEF	X	1				yes
DEF	UNDEF	X	0				yes
UNDEF	X	DEF	X				yes
UNDEF	X	UNDEF	X

# Web resources

#### CIA : Can in Automation
Many documentation on CANopen.
http://www.can-cia.de

#### Resources and training in CANopen
http://www.esacademy.com

#### Elektronikladen HCS12 T-board
http://www.elektronikladen.de/en_hcs12tb.html

#### Gnu gcc compiler for HC12
http://m68hc11.serveftp.org/m68hc11_port.php

#### Motorola documentation on HC12
http://www.freescale.com/webapp/sps/site/prod_summary.jsp?code=MC9S12DP256

#### Lauterbach debugger for HC12
http://www.lauterbach.com

#### Python language
http://www.python.org

##### Jaxe, XML editor written in Java
http://jaxe.sourceforge.net

# About this project ...

This project was written by :

Unité mixte de recherche INRETS-LCPC
sur les Interractions Véhicule-Infrastructure-Conducteur
14, route de la minière
78000 Versailles
Tel : 01 40 43 29 01
http://www.inrets.fr/ur/livic
Contributors :	Francis DUPIN
Camille BOSSARD
Laurent ROMIEUX

204, rue du Haut du Pin
88470 Saint-Michel sur Meurthe
Tel : 03 29 52 95 67
http://www.lolitech.fr
Contributors :	Edouard TISSERANT (Original author)
Laurent BESSARD

Many thanks to the other contributors for their great work:
Raphael ZULLIGER
David DUMINY (sté A6R)
Zakaria BELAMRI